## Slide 1: T06 - Smart Cane System Modelling
Members: Dusan Micic, Shadman Samin, Nathan Pham, Keon Yoo
Document ID: T06_Model_V1 Version : 1.0
Date : 11/13/2015
Location : Git Wiki Page

## Slide 2: Level - 0 Diagram
Smart Cane
Ultrasonic Sensors Input
Power, 9 V
Haptic Motor Output
LED Output
Module | Smart Cane
Inputs | The system has two inputs coming in a 3 bit Input from 3 Ultrasonic Sensor. Each containing a bit wide pulses that gives us distance information based on the width of the pulse. Second, we have the 9 V Power that is connected to the 9 V battery that powers the whole system.
Outputs | Digital Ouptuts to Haptic Motor and LED output
Functionality | Measure the distance between the user and nearby object. And notifies the user if the object is too close.
3 bit

## Slide 3: Level - 0: 5 V Regulator
Regulator: 5 V
5 V (Analog DC)
Module | Regulator: 5 V
Inputs | Battery connection with a +9 V DC Battery (Analog)
Outputs | +5 V DC Output (Analog), Maximum Current: 1 A
Functionality | Output a constant 5 V output from a 9 V
Power, 9 V

## Slide 4: Level - 0: 3.3 V Regulator
Regulator: 3.3 V
3.3 V (Analog DC)
Module | Regulator: 5 V
Inputs | Battery connection with a +9 V DC Battery (Analog)
Outputs | +3.3 V DC Output (Analog), Maximum Current: 1 A
Functionality | Output a constant 3.3 V output from a 9 V
Power, 9 V

## Slide 5: Level - 0: Ultrasonic
Ultrasonic
Digital Input/Output
Module | Regulator: 5 V
Inputs | 5 V DC Input (Analog)
I/O (Input/Output) Pin | The Microprocessors sends a digital trigger to the ultrasonic to activate it. The sensor sends back a digital pulse on the same pin to the microprocessor.
Functionality | Every 100 ms the sensor receive a 10 us trigger to activate it and send back a digital pulse to the microcontroller which contains distance information.
5 V Input

## Slide 6: Level - 0: Microprocessor
Microprocessor
Digital Output (LED)
Module | Regulator: 5 V
Inputs | 5 V DC Input (Analog) Digital Input/Output Connection to the Ultrasonic Sensors
Outputs | Digital Output to run the Motor circuit and the LED’s to notify the users of oncoming obstacles
Functionality | When the microcontroller gets an input from the Ultrasonic sensors it looks at the width of the return pulse to find the distance between the user the object in front. If the distance is less than the safe distance the Digital pins on the outputs go High to notify the user.
Digital Input/Output
Regulator: 5 V
Digital Output (Motors)

## Slide 7: Level - 0: Microprocessor
Haptic Motors
Module | Regulator: 5 V
Inputs | 3.3 V DC Input (Analog) Digital Input Connection from Microprocessor
Outputs | Haptic Vibration
Functionality | If the Sensors detect an object too close to the user the Microprocessor sends a high bit through one of the digital ports to turn on the Haptic motors to warn the user.
Digital Input
3.3 V

## Slide 8: Level 1: Smart Cane
Application Software
SPI Interface Program & Debug
Regulator: 5 V
Regulator: 3.3 V
9 V Battery
Microprocessor
Ultrasonic-1
Ultrasonic-2
Ultrasonic-3
Digital Input/Output
Digital Input/Output
Digital Input/Output
Reset
LED (optional)
Haptic Motors
Digital Output
Digital Output

## Slide 9: Smart Cane Flowchart Representation
Start
Object Detection
Calculate the distance between Object and Cane
Distance < 30 cm
No
Turn on the LED and Haptic Motors to Alert the User
End
Yes

## Slide 10: State Machine View
No object detected
Object detected
User Feedback LED and Motor
Verify Distance