## Slide 1: T06 - Smart Cane System Modelling
Members: Dusan Micic, Shadman Samin, Nathan Pham, Keon Yoo
Document ID: T06_Model_V1 Version : 1.1
Date : 12/9/2015
Location : Git Wiki Page

## Slide 2: Level - 0 Diagram
Smart Cane
3 different Ultrasonic Sensor Inputs
Power, 9V DC
Haptic Motor Output
Module | Smart Cane
Inputs | The system has three pulse width inputs coming in from 3 Ultrasonic Sensors. Each containing an 8 cycle burst pulses that gives us distance information based on the width of the pulse. Second, we have the 9V DC Power that is connected to the 9V battery that powers the whole system.
Outputs | Digital Output to Haptic Motor for operation
Functionality | Measure the distance between the user and nearby objects. And notifies the user if the object is too close.

## Slide 3: Level 1: Smart Cane
Application Software
SPI Interface Program & Debug
Regulator: 5V
Regulator: 3.3V
9V Battery
Microprocessor
Ultrasonic-1
Ultrasonic-2
Ultrasonic-3
Digital Input/Output
Digital Input/Output
Digital Input/Output
Haptic Motors
Digital Output
Digital Input/Output

## Slide 4: Level - 0: 5V Regulator
Regulator: 5V
5 V (DC)
Module | Regulator: 5V
Inputs | Battery connection with a +9V DC Battery
Outputs | +5V DC Output, Maximum Current: 1A
Functionality | Output a constant 5V DC output from a 9 V
Power, 9V DC

## Slide 5: Level - 0: 3.3V Regulator
Regulator: 3.3V
3.3V (Analog DC)
Module | Regulator: 3.3V
Inputs | Battery connection with a +9V DC Battery
Outputs | +3.3V DC Output, Maximum Current: 1A
Functionality | Output a constant 3.3V output from a 9V
Power, 9V DC

## Slide 6: Level - 0: Ultrasonic Sensor
Ultrasonic Sensor
Digital Input/Output
Module | Ultrasonic Sensor
Inputs | 5V DC Input for the Ultrasonic Sensor(From 5V Voltage Regulator)
I/O (Input/Output) Pin | The Microprocessors sends a digital trigger pulse (5V) to the ultrasonic sensor to activate it. The sensor sends back an echo signal by an 8 cycle burst pulse (~5V) on the same pin to the microprocessor. The width of the digital pulse to the microprocessor indicates the obstruction distance. The wider the signal the further the object.
Functionality | Every 100 ms the sensor receive a 10 us trigger to activate it and send back a digital pulse to the microcontroller which contains distance information.
5V DC, Power

## Slide 7: Level - 0: Microprocessor
Microprocessor
Module | Microprocessor
Inputs | 5V DC Input for Power (From 5V Regulator) Input 8 burst cycle from the echo of ultrasonic sensor to detect distance.
Outputs | Send output high (~5V) to bias transistor allowing current flow to power motor on when within obstruction distance Output 10us pulse high (~5V) to trigger the Ultrasonic sensors
Functionality | When the microcontroller gets an input from the Ultrasonic sensors it looks at the width of the return pulse to find the distance between the user the object in front. If the distance is less than the safe distance the Digital pins on the outputs go High to notify the user.
Digital Input/Output
5V DC, Power
Digital Output (Motors)

## Slide 8: Level - 0: Haptic Motor
Haptic Motor
Module | Haptic Motor
Inputs | 3.3V DC Input (from 3.3V Voltage Regulator) Digital Input Connection from Microprocessor (output high ~5 volts)
Outputs | Motor Vibration Output
Functionality | If the Sensors detect an object too close to the user the Microprocessor sends a high bit through one of the digital ports on the microprocessor to turn on the Haptic motors (4.5 – 3.0 Volt required power to operate) to warn the user of an obstruction.
Digital Input
3.3V DC, Power
Motor Vibration Output

## Slide 9: Smart Cane Flowchart Representation
Start
Object Detection
Calculate the distance between Object and Cane
Distance < 30 cm
No
Turn on the LED and Haptic Motors to Alert the User
Yes
Distance < 30 cm
Yes
No

## Slide 10: State Machine View
No object detected
Within Motor distance
User Feedback and Operate Motor
Verify Distance
Object Detection
object detected
Not within motor distance
Re-verify distance